## Slide 1: Creating J.A.R.V.I.S.

## Slide 2: Creating J.A.R.V.I.S.
An Awesome Guide To Automating Your Home
By Scott Preston

## Slide 3: About Me
Live in Columbus, Ohio.
Been doing robotics for last 15 years
Wrote a few books on robotics and mobile/js/html5.
Practice Lead at ICC focusing on JavaScript
I’ll be at ICC booth after this talk pairing with JR.
First brought my robot to CodeMash in 2009.

## Slide 4: What’s J.A.R.V.I.S. stand for?

## Slide 5: J.A.R.V.I.S.
J – Just
A – A
R – Rather
V – Very
I – Intelligent
S - System

## Slide 6: About J.A.R.V.I.S.
Ubuntu Server 12.04
Core i5 / 16GB Ram / 240GB SSD
1GB Ethernet / 1 Bluetooth
4 USB Serial Ports
4 Slave Raspberry PIs w/LIRC & Temp Sensors
9 Network Cameras
1 Windows Machine for Skype
@jarvispreston (Twitter Handle)

## Slide 7: How did I get here?

## Slide 8: Summer 2008

## Slide 9: Initial Goals
Turn lights on/off Sunrise / Sunset
Wake me up with weather report

## Slide 10: I had an old robot (JR-MK2)

## Slide 11: Robot Had 2 Parts I needed
Basic Stamp & Distribution Board
Serial Servo Controller

## Slide 12: Stamp & Controller Board

## Slide 13: SSC

## Slide 14: Before X10 ~ $7 Switch

## Slide 15: Used SSC (Still Used)
Lights On
http://192.168.1.60:8001/?pin=2&pos=200
http://192.168.1.60:8001/?pin=3&pos=70
Lights Off
http://192.168.1.60:8001/?pin=2&pos=127
http://192.168.1.60:8001/?pin=3&pos=127

## Slide 16: X10 – External Lights

## Slide 17: What’s X10?
Developed in 1975 by Pico Electronics (Scotland)
Digital Carrier transmitted onto a 120hz carrier existing power lines.
Limitations – GCFI Outlets, Older Technology, Reliability, # of Devices
Pros – Cheap, Nothing else around in 2008, Microcontrollers have built-in support

## Slide 18: X10 – TW523 Interface~$60-$80

## Slide 19: X10 – WS467 $16.99

## Slide 20: X10 – Protocol (via BS2)
XOUT mPin, zPin, [houseCode\unitCode]
XOUT mPin, xPin, [houseCode\onORoff]
houseCode = 1-16
unitCode = 1-16
onORoff = 0, 1

## Slide 21: Initial Layout

## Slide 22: Node Set-Up
npm install serial-port (Serial Ports)
npm install serial-servo (Serial Servo Controllers)

## Slide 23: X10.js – SerialPort
var http = require('http');
var url = require('url');
var port = 8000;
var usbport = "/dev/ttyUSB0";
var SerialPort = require("serialport").SerialPort;
var sp = new SerialPort(usbport, {
baudrate: 9600
});
Serial Port Setup

## Slide 24: X10.js – Server Code
var server = http.createServer(function (request, response) {
var url_parts = url.parse(request.url, true);
var house = url_parts.query.house;
var device = url_parts.query.device;
var onoff = url_parts.query.onoff;
write(house,device,onoff);
});
Http Parms to Serial Port

## Slide 25: X10.js – Serial Writing
function write(house, device, onoff) {
if (house >= 0 && device >= 0 && onoff >= 0) {
var b = [100, house, device, onoff];
sp.write(b);
}
}
Byte[] sent to serial port

## Slide 26: Sunrise & Sunset
http://api.wunderground.com/api/USER_KEY/astronomy/q/43212.json
Gets sun-rise
Gets sun-set
CRON runs each minute and checks for time match

## Slide 27: Weather Underground – REST API
http://api.wunderground.com/api/USER_KEY/conditions/q/43212.json
Schedule Via CRON (hourly)
Populate to database via wrapper.

## Slide 28: Putting It All Together
Old Robot Parts w/Serial & X10
X10 Switches
Weather Underground w/Sunrise & Sunset Data
CRON Scheduler
Results: Robot that can turn on/off lights for me.
Missing: Text-To-Speech (later)

## Slide 29: More Devices
Since X10 is 40 years old

## Slide 30: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 31: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 32: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 33: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 34: Device Types
Controllers
Locks
Thermostats
Sensors
Lights
Switches
Smart Meters

## Slide 35: Proprietary - IRIS by Lowes
Some devices Z-Wave Compatible!

## Slide 36: Schlage Z-wave Lock

## Slide 37: KEVO – Bluetooth LE (Not Z-Wave)

## Slide 38: Kwickset – Z-Wave

## Slide 39: nest Thermostat ($250)
REST API available from nest and full SDK.

## Slide 40: Z-Wave + WiFi ~$75 to $200

## Slide 41: Aeon Labs – Z-Wave Switch

## Slide 42: Phillips Hue (Zigbee & Ethernet)
http://www.developers.meethue.com/tools-and-sdks

## Slide 43: WeMo – WiFi Switch
Many NPM modules available to use.

## Slide 44: Z-Wave Flood Sensor

## Slide 45: Z-wave Interfacing

## Slide 46: Raspberry Pi ~ $30

## Slide 47: Z-Wave GPIO Daughter Card - $60
http://razberry.z-wave.me/

## Slide 48: Z-Wave USB ~$40
Google ‘openzwave’ for npm modules.

## Slide 49: How close are we to J.A.R.V.I.S.?

## Slide 50: J.A.R.V.I.S.
Home Sensors
Home Control (Lights/Blinds/Etc.)
Speech Recognition / Text-To-Speech
Computer Vision
TV / Stereo Control
Event Based System & Robot Control
3D Metal Printers

## Slide 51: Speech Recognition
w/Sphinx4
Open Source Java Speech Recognition

## Slide 52: Wrote this book in 2005.

## Slide 53: SR – Part 1 (Chapter 6)
while (true) { Result result = recognizer.recognize(); if (result != null) { String resultText = result.getBestFinalResultNoFiller(); JarvisUtils.logger("I heard: " + resultText); String recognizerURL = "http://192.168.1.60/voice/respond/"; ApacheHttp.postSingleString(recognizerURL,"txt",resultText); JarvisUtils.pause(2000); // wait a second before listening again } }
Gets “best” result

## Slide 54: SR – Part 1 (Chapter 6)
while (true) { Result result = recognizer.recognize(); if (result != null) { String resultText = result.getBestFinalResultNoFiller(); JarvisUtils.logger("I heard: " + resultText); String recognizerURL = "http://192.168.1.60/voice/respond/"; ApacheHttp.postSingleString(recognizerURL,"txt",resultText); JarvisUtils.pause(2000); // wait a second before listening again } }
Passes to service for response & TTS

## Slide 55: Before 2014
Each Call To Specific Words  Map to specific URLs
Each time I wanted to update, I had to re-compile, and updated.
I wanted something more dynamic.
if command1, call service1, if command2, call service2

## Slide 56: Early 2014
Sent words to service.
Service mapped words to new service endpoints.

## Slide 57: Late 2014
Changed from service mappings to event publish via RabbitMQ

## Slide 58: Text To Speech
3rd Party Voice (Cepstral TTS)
Festival TTS (Free)
Linux command I’m using:
/usr/bin/padsp swift “words to speak”

## Slide 59: Remote Text To Speech
swift "$1" -o tmp.wav // create wav
lame tmp.wav tmp.mp3 // convert to mp3
scp tmp.mp3 pi@10.10.10.32:tmp.mp3 // send
ssh pi@10.10.10.32 'mpg123 tmp.mp3' // play

## Slide 60: Remote Text To Speech
swift "$1" -o tmp.wav // create wav
lame tmp.wav tmp.mp3 // convert to mp3
scp tmp.mp3 pi@10.10.10.32:tmp.mp3 // send
ssh pi@10.10.10.32 'mpg123 tmp.mp3' // play

## Slide 61: Remote Text To Speech
swift "$1" -o tmp.wav // create wav
lame tmp.wav tmp.mp3 // convert to mp3
scp tmp.mp3 pi@10.10.10.32:tmp.mp3 // send
ssh pi@10.10.10.32 'mpg123 tmp.mp3' // play

## Slide 62: Remote Text To Speech
swift "$1" -o tmp.wav // create wav
lame tmp.wav tmp.mp3 // convert to mp3
scp tmp.mp3 pi@10.10.10.32:tmp.mp3 // send
ssh pi@10.10.10.32 'mpg123 tmp.mp3' // play

## Slide 63: How do I talk to J.A.R.V.I.S.?
Microphone
Wireless Headset
Bluetooth
Skype via API?
Skype as Services??

## Slide 64: Skype As Service (low-tech)

## Slide 65: Putting It all Together
Speech Recognition – Publishing Events
Text To Speech either via Speaker, Skype (Phone) or Remote Speaker
Tell J.A.R.V.I.S. to turn on lights and turn off lights

## Slide 66: J.A.R.V.I.S Voice Demo

## Slide 67: What Next?

## Slide 68: Computer Vision
9 Network Cameras in Total
To Report Motion Detection Events
Each capable of doing face recognition (still debugging)
J.A.R.V.I.S. – Using Java based motion detection in multiple threads for each camera defined via UI
Table of Camera Stored in J.A.R.V.I.S Database

## Slide 69: Foscam Pan/Tilt
Resolution 640x480 and 1280x720

## Slide 70: Camera Parameters
Name
Snapshot_url for taking JPG image
Sample Frequency in milliseconds
Sensitivity
Top, Left, Height, Width
Notify URL / Event To Publish

## Slide 71: Vision Summary
9 Cams Mapped To Location
J.A.R.V.I.S. monitors “motion” events and “face” events
Checks For Motion every 500ms to 2000ms
Face checks only if motion

## Slide 72: TV / Stereo Control
Device Might Have an API
LIRC w/Raspberry PI

## Slide 73: DirecTV - Power On
http://192.168.1.99:8080/remote/processKey?key=poweron&hold=keyPress

## Slide 74: DirecTV – Power Off
http://192.168.1.99:8080/remote/processKey?key=poweroff&hold=keyPress

## Slide 75: DirecTV – Change Channel
http://192.168.1.99:8080/tv/tune?major=10

## Slide 76: Sparkfun – Max Power LED $2.95

## Slide 77: LIRC
Linux Infrared Remote Control - http://www.lirc.org/
apt-get install lirc
update /etc/modules
update /etc/lirc/hardware.conf
update /etc/lirc/lircd.conf

## Slide 78: Invoking From Service
Use php exec(garage-power.sh)
#!/bin/bash ssh pi@10.10.10.32 'irsend SEND_ONCE yam POWER'
** Subscribe to STEREO_ON event, calls shell

## Slide 79: LIRC Diagram
Raspberry PI GPIO

## Slide 80: lircd.conf
begin remote
name yam
bits 32
flags SPACE_ENC
eps 20
aeps 200
header 8800 4400
one 550 1650
zero 550 550
ptrail 550
repeat 8800 2200
gap 38500
toggle_bit 0
frequency 38000
begin codes
POWER 0x000000005EA1F807

## Slide 81: Garage Wiring Diagram

## Slide 82: Garage Behavior
PUBLISHERS (garage-pi)
If (open) publish (‘garage-door-open’)
CONSUMERS (garage-pi, jarvis, feynman)
turn on PC
greet via tts
turn on garage lights,
turn on garage TV or Stereo (different rules)

## Slide 83: Final Step
Event Based Architecture

## Slide 84: Why Events?
Everything that’s happening is some kind of event.
Multiple subscribers to events - jarvis, tvroom-pi, garage-pi, basement-pi, feynman-jr, feynman (in garage)
One places to control event processing vs. in each app

## Slide 85: Before Events
Speech Recognition – Mapped to services, words were hard coded, each update required new java compile.
Hard coded URLS everywhere – 4 Pis, new functionality, required going everywhere and updating service definition.
Chains of Services (IF-THIS-THEN-THAT) IFTTT required going lots of places

## Slide 86: NodeJS Installation
npm install amqp

## Slide 87: RabbitMQ - Installation
apt-get install rabbitmq-server

## Slide 88: Dynamically Load Event Rules
{ "name": "test", "events": [ { "name": "broadcast", "data": { "endpoints": [ "http://www.google.com", "http://www.scottpreston.com"] } }, { "name": "notify", "data": { "message": "tested google and scottpreston" } } ]}

## Slide 89: Dynamically Load Event Rules
{ "name": "test", "events": [ { "name": "broadcast", "data": { "endpoints": [ "http://www.google.com", "http://www.scottpreston.com"] } }, { "name": "notify", "data": { "message": "tested google and scottpreston" } } ]}
Event Name
(What’s Published)

## Slide 90: Dynamically Load Event Rules
{ "name": "test", "events": [ { "name": "broadcast", "data": { "endpoints": [ "http://www.google.com", "http://www.scottpreston.com"] } }, { "name": "notify", "data": { "message": "tested google and scottpreston" } } ]}
Event Type

## Slide 91: Dynamically Load Event Rules
{ "name": "test", "events": [ { "name": "broadcast", "data": { "endpoints": [ "http://www.google.com", "http://www.scottpreston.com"] } }, { "name": "notify", "data": { "message": "tested google and scottpreston" } } ]}
Event Data

## Slide 92: Putting It All Together

## Slide 93: Event-server.js
function createConnection() { var connection = amqp.createConnection({host: 'localhost'}); connection.on('ready', function () { connection.exchange('house', { type: 'fanout', autoDelete: false }, function (exchange) { connection.queue('tmp-' + Math.random(), {exclusive: true}, function (queue) { queue.bind('house', ''); console.log(' [*] Waiting for house events. To exit press CTRL+C') queue.subscribe(function (msg) { var message = msg.data.toString('utf-8'); console.log("message received = " + message); var eventDetail = JSON.parse(message); processEvent(eventDetail.name, eventDetail.data); }); }) }); }); }
Create Connection

## Slide 94: Event-server.js
function createConnection() { var connection = amqp.createConnection({host: 'localhost'}); connection.on('ready', function () { connection.exchange('house', { type: 'fanout', autoDelete: false }, function (exchange) { connection.queue('tmp-' + Math.random(), {exclusive: true}, function (queue) { queue.bind('house', ''); console.log(' [*] Waiting for house events. To exit press CTRL+C') queue.subscribe(function (msg) { var message = msg.data.toString('utf-8'); console.log("message received = " + message); var eventDetail = JSON.parse(message); processEvent(eventDetail.name, eventDetail.data); }); }) }); }); }
Process Event

## Slide 95: Event-server.js - Continued
handledEvents.broadcast = function (endpoint) { if (endpoint) { request(endpoint, function (error, response, body) { …
}); } };
Event Handler
(to make http call to service)

## Slide 96: Non-Local Events - SQS

## Slide 97: J.A.R.V.I.S & Feynman JR. DEMO

## Slide 98: Thank You
@scottpreston
Http://github.com/scottpreston