## Slide 1: Creating J.A.R.V.I.S.

## Slide 2: Creating J.A.R.V.I.S.
An Awesome Guide To Automating Your Home
By Scott Preston

## Slide 4: About Me
Live in Columbus, Ohio.
Been doing robotics for last 15 years
Wrote a few books on robotics and mobile/js/html5.
Practice Lead at ICC focusing on JavaScript
Robotics Talks: COJUG, CRB, CodeMash, Ohio Linux

## Slide 5: What’s J.A.R.V.I.S. stand for?

## Slide 6: J.A.R.V.I.S.
J – Just
A – A
R – Rather
V – Very
I – Intelligent
S - System

## Slide 7: About J.A.R.V.I.S.
Ubuntu Server 14.04
Core i5 / 16GB Ram / 240GB SSD
1GB Ethernet / 1 Bluetooth
4 USB Serial Ports
6 Slave Raspberry PIs w/LIRC & Temp Sensors
9 Network Cameras
1 Windows Machine for Skype
@jarvispreston (Twitter Handle)

## Slide 8: How did I get here?

## Slide 9: Summer 2008

## Slide 10: Initial Goals
Turn lights on/off Sunrise / Sunset
Wake me up with weather report

## Slide 11: I had an old robot (JR-MK2)

## Slide 12: Robot Had 2 Parts I needed
Basic Stamp & Distribution Board
Serial Servo Controller

## Slide 13: Stamp & Controller Board

## Slide 14: SSC

## Slide 15: Before X10 ~ $7 Switch

## Slide 16: Used SSC (Still Used)
Lights On
http://192.168.1.60:8001/?pin=2&pos=200
http://192.168.1.60:8001/?pin=3&pos=70
Lights Off
http://192.168.1.60:8001/?pin=2&pos=127
http://192.168.1.60:8001/?pin=3&pos=127

## Slide 17: X10 – External Lights

## Slide 18: What’s X10?
Developed in 1975 by Pico Electronics (Scotland)
Digital Carrier transmitted onto a 120hz carrier existing power lines.
Limitations – GCFI Outlets, Older Technology, Reliability, # of Devices
Pros – Cheap, Nothing else around in 2008, Microcontrollers have built-in support

## Slide 19: X10 – TW523 Interface~$60-$80

## Slide 20: X10 – WS467 $16.99

## Slide 21: X10 – Protocol (via BS2)
XOUT mPin, zPin, [houseCode\unitCode]
XOUT mPin, xPin, [houseCode\onORoff]
houseCode = 1-16
unitCode = 1-16
onORoff = 0, 1

## Slide 22: Initial Layout

## Slide 23: Node Set-Up
npm install serial-port (Serial Ports)
npm install serial-servo (Serial Servo Controllers)

## Slide 24: X10.js – SerialPort
var http = require('http');
var url = require('url');
var port = 8000;
var usbport = "/dev/ttyUSB0";
var SerialPort = require("serialport").SerialPort;
var sp = new SerialPort(usbport, {
baudrate: 9600
});
Serial Port Setup

## Slide 25: X10.js – Server Code
var server = http.createServer(function (request, response) {
var url_parts = url.parse(request.url, true);
var house = url_parts.query.house;
var device = url_parts.query.device;
var onoff = url_parts.query.onoff;
write(house,device,onoff);
});
Http Parms to Serial Port

## Slide 26: X10.js – Serial Writing
function write(house, device, onoff) {
if (house >= 0 && device >= 0 && onoff >= 0) {
var b = [100, house, device, onoff];
sp.write(b);
}
}
Byte[] sent to serial port

## Slide 27: Sunrise & Sunset
http://api.wunderground.com/api/USER_KEY/astronomy/q/43212.json
Gets sun-rise
Gets sun-set
CRON runs each minute and checks for time match

## Slide 28: Weather Underground – REST API
http://api.wunderground.com/api/USER_KEY/conditions/q/43212.json
Schedule Via CRON (hourly)
Populate to database via wrapper.

## Slide 29: Putting It All Together
Old Robot Parts w/Serial & X10
X10 Switches
Weather Underground w/Sunrise & Sunset Data
CRON Scheduler
Results: Robot that can turn on/off lights for me.
Missing: Text-To-Speech (later)

## Slide 30: More Devices
Since X10 is 40 years old

## Slide 31: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 32: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 33: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 34: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 35: Kinds Of Devices (non-X10)
Proprietary (Lots of these) – On their own
Wifi – Many devices, limited APIs & Smart Phones
BLE – Blue Tooth Low Energy (Smart Phone Only)
Z-Wave – Need Interface (Wireless)
Insteon – Need Interface module Wireless + X10

## Slide 36: Device Types
Controllers/Hubs
Locks
Thermostats
Sensors
Lights
Switches
Smart Meters

## Slide 37: Proprietary - IRIS by Lowes
Some devices Z-Wave Compatible!

## Slide 38: Schlage Z-wave Lock

## Slide 39: KEVO – Bluetooth LE (Not Z-Wave)

## Slide 40: Kwickset – Z-Wave

## Slide 41: nest Thermostat ($250)
REST API available from nest and full SDK.

## Slide 42: Z-Wave + WiFi ~$75 to $200

## Slide 43: Radio Thermostat ~$100 with REST API from Amazon.Com

## Slide 44: Aeon Labs – Z-Wave Switch

## Slide 45: Phillips Hue (Zigbee & Ethernet)
http://www.developers.meethue.com/tools-and-sdks

## Slide 46: WeMo – WiFi Switch
Many NPM modules available to use.

## Slide 47: Z-Wave Flood Sensor

## Slide 48: Z-wave Interfacing

## Slide 49: Raspberry Pi ~ $30

## Slide 50: Z-Wave GPIO Daughter Card - $60
http://razberry.z-wave.me/

## Slide 51: Z-Wave USB ~$40
Google ‘openzwave’ for npm modules.

## Slide 52: How close are we to J.A.R.V.I.S.?

## Slide 53: J.A.R.V.I.S.
Home Sensors
Home Control (Lights/Blinds/Etc.)
Speech Recognition / Text-To-Speech
Computer Vision
TV / Stereo Control
Event Based System & Robot Control
3D Metal Printers

## Slide 54: Speech Recognition
w/Sphinx4
Open Source Java Speech Recognition

## Slide 55: Wrote this book in 2005.

## Slide 56: Text To Speech
3rd Party Voice (Cepstral TTS)
Festival TTS (Free)
Linux command I’m using:
/usr/bin/padsp swift “words to speak”

## Slide 57: Remote Text To Speech
swift "$1" -o tmp.wav // create wav
lame tmp.wav tmp.mp3 // convert to mp3
scp tmp.mp3 pi@10.10.10.32:tmp.mp3 // send
ssh pi@10.10.10.32 'mpg123 tmp.mp3' // play

## Slide 58: Remote Text To Speech
swift "$1" -o tmp.wav // create wav
lame tmp.wav tmp.mp3 // convert to mp3
scp tmp.mp3 pi@10.10.10.32:tmp.mp3 // send
ssh pi@10.10.10.32 'mpg123 tmp.mp3' // play

## Slide 59: Remote Text To Speech
swift "$1" -o tmp.wav // create wav
lame tmp.wav tmp.mp3 // convert to mp3
scp tmp.mp3 pi@10.10.10.32:tmp.mp3 // send
ssh pi@10.10.10.32 'mpg123 tmp.mp3' // play

## Slide 60: Remote Text To Speech
swift "$1" -o tmp.wav // create wav
lame tmp.wav tmp.mp3 // convert to mp3
scp tmp.mp3 pi@10.10.10.32:tmp.mp3 // send
ssh pi@10.10.10.32 'mpg123 tmp.mp3' // play

## Slide 61: How do I talk to J.A.R.V.I.S.?
Microphone
Wireless Headset
Bluetooth
Skype via API?
Skype as Services??

## Slide 62: Skype As Service (low-tech)

## Slide 63: Putting It all Together
Speech Recognition – Publishing Events
Text To Speech either via Speaker, Skype (Phone) or Remote Speaker
Tell J.A.R.V.I.S. to turn on lights and turn off lights

## Slide 64: J.A.R.V.I.S Voice Demo

## Slide 65: What Next?

## Slide 66: Computer Vision
9 Network Cameras in Total
To Report Motion Detection Events
Each capable of doing face recognition (still debugging)
J.A.R.V.I.S. – Using Java based motion detection in multiple threads for each camera defined via UI
Table of Camera Stored in J.A.R.V.I.S Database

## Slide 67: Foscam Pan/Tilt
Resolution 640x480 and 1280x720

## Slide 68: Camera Parameters
Name
Snapshot_url for taking JPG image
Sample Frequency in milliseconds
Sensitivity
Top, Left, Height, Width
Notify URL / Event To Publish

## Slide 69: Vision Summary
9 Cams Mapped To Location
J.A.R.V.I.S. monitors “motion” events and “face” events
Checks For Motion every 500ms to 2000ms
Face checks only if motion

## Slide 70: TV / Stereo Control
Device Might Have an API
LIRC w/Raspberry PI

## Slide 71: DirecTV - Power On
http://192.168.1.99:8080/remote/processKey?key=poweron&hold=keyPress

## Slide 72: DirecTV – Power Off
http://192.168.1.99:8080/remote/processKey?key=poweroff&hold=keyPress

## Slide 73: DirecTV – Change Channel
http://192.168.1.99:8080/tv/tune?major=10

## Slide 74: Sparkfun – Max Power LED $2.95

## Slide 75: LIRC
Linux Infrared Remote Control - http://www.lirc.org/
apt-get install lirc
update /etc/modules
update /etc/lirc/hardware.conf
update /etc/lirc/lircd.conf

## Slide 76: Invoking From Service
Use php exec(garage-power.sh)
#!/bin/bash ssh pi@10.10.10.32 'irsend SEND_ONCE yam POWER'
** Subscribe to STEREO_ON event, calls shell

## Slide 77: LIRC Diagram
Raspberry PI GPIO

## Slide 78: lircd.conf
begin remote
name yam
bits 32
flags SPACE_ENC
eps 20
aeps 200
header 8800 4400
one 550 1650
zero 550 550
ptrail 550
repeat 8800 2200
gap 38500
toggle_bit 0
frequency 38000
begin codes
POWER 0x000000005EA1F807

## Slide 79: Garage Wiring Diagram

## Slide 80: Non-Local Events - SQS

## Slide 81: J.A.R.V.I.S & Feynman JR. DEMO

## Slide 82: CodeMash 2.0.1.6.

## Slide 83: Thank You
@scottpreston
Http://github.com/scottpreston